## Slide 1: Image filters and morphometric operators Elnaz Fazeli
29.2-3.3, 2020
Centre Broca Nouvelle-Aquitaine, Bordeaux, France
Training School # 14 BioImage Analysis for Early Career Investigators “Image processing and analysis using Fiji and ilastik”
Adopted from
Fabrice P. Cordelières slides Christian Tischer
Paulo de Castro Aguiar
Olivier Burri, Romain Guiet & Arne Seitz

## Slide 2: During the lecture
1
How to use linear filtering
Practice with ImageJ Fiji convolve tool
Practice with filters
2
How to use RANK filtering
Practice with ImageJ Fiji RANK filters
3
Practical exercises
Trying uneven background subtraction
Trying noise removal using filters
4
Morphological operators
Trying different morphological operators

## Slide 3: What are images
Images/1-osteoclast.tif
Quick recap of what are images
Notes: Pixel inspector
Tif
Txt
And histogram

## Slide 4: During the lecture
1
How to use linear filtering
Practice with ImageJ Fiji convolve tool
Practice with filters

## Slide 5: What are images, as Fabrice also said
An image is…
a collection of
pixels
a collection of
frequencies
Independent
pixels
Pixels within a
neighbourhood
a collection of
objects
Histogram manipulations
Spatial filtering
Frequential filtering
Connecitviy analysis
&
morphometry

## Slide 6: Images as a collection of pixels
Input image
Segmentation or connectivity analysis
Histogram manipulations
Spatial
filtering
Frequential
filtering
Pre-processing
Alone or as a sequence
Notes: Ex:
Histogram stretching
Histogram equalization
Gamma
Median filtering
Gaussian filtering
DoG/LoG filtering
Sobel filtering
Filtering in Fourier domain
…

## Slide 7: Image filtering
Enhancing image features prior to image analysis.
The purpose is to improve the segmentation accuracy and efficiency, as well as ”beautifying images!”.
It is important to know what you are doing as you are changing the original data by performing any filters.

## Slide 8: Linear spatial filters
1 | 0 | 1 | 1 | 0
0 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
Simple image matrix
1/9 | 1/9 | 1/9
1/9 | 1/9 | 1/9
1/9 | 1/9 | 1/9
Averaging kernel
Linear: every new pixel is a linear combination of the corresponding pixel in the original image and its neighbors

## Slide 9: Linear spatial filters
1 | 0 | 1 | 1 | 0
0 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
Simple image matrix
x1/9 | x1/9 | x1/9
x1/9 | x1/9 | x1/9
x1/9 | x1/9 | x1/9
Output matrix
(1x1/9) + (0x1/9) + (1x1/9) + (0x1/9) + (0x1/9) + (1x1/9) + (1x1/9) + (1x1/9) + (1x1/9) = 6/9 = 0.67
0.67 |  | 

## Slide 10: Linear spatial filters
1 | 0 | 1 | 1 | 0
0 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
Simple image matrix
x1/9 | x1/9 | x1/9
x1/9 | x1/9 | x1/9
x1/9 | x1/9 | x1/9
Output matrix
(1x1/9) + (0x1/9) + (1x1/9) + (0x1/9) + (0x1/9) + (1x1/9) + (1x1/9) + (1x1/9) + (1x1/9) = 6/9 = 0.67
0.67 | 0.67 | 

## Slide 11: Linear spatial filters
1 | 0 | 1 | 1 | 0
0 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
Simple image matrix
x1/9 | x1/9 | x1/9
x1/9 | x1/9 | x1/9
x1/9 | x1/9 | x1/9
Output matrix
(1x1/9) + (1x1/9) + (0x1/9) + (1x1/9) + (0x1/9) + (1x1/9) + (1x1/9) + (1x1/9) + (1x1/9) = 7/9 = 0.78
0.67 | 0.67 | 0.78

## Slide 12: Linear spatial filters
1 | 0 | 1 | 1 | 0
0 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
Simple image matrix
x1/9 | x1/9 | x1/9
x1/9 | x1/9 | x1/9
x1/9 | x1/9 | x1/9
Output matrix
(0x1/9) + (0x1/9) + (1x1/9) + (1x1/9) + (1x1/9) + (1x1/9) + (0x1/9) + (1x1/9) + (0x1/9) = 5/9 = 0.56
0.67 | 0.67 | 0.78
0.56 |  | 

## Slide 13: Linear spatial filters
1 | 0 | 1 | 1 | 0
0 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
Simple image matrix
x1/9 | x1/9 | x1/9
x1/9 | x1/9 | x1/9
x1/9 | x1/9 | x1/9
Output matrix
(0x1/9) + (1x1/9) + (0x1/9) + (1x1/9) + (1x1/9) + (1x1/9) + (1x1/9) + (0x1/9) + (1x1/9) = 6/9 = 0.67
0.67 | 0.67 | 0.78
0.56 | 0.67 | 

## Slide 14: Linear spatial filters
1 | 0 | 1 | 1 | 0
0 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
Simple image matrix
x1/9 | x1/9 | x1/9
x1/9 | x1/9 | x1/9
x1/9 | x1/9 | x1/9
Output matrix
(1x1/9) + (0x1/9) + (1x1/9) + (1x1/9) + (1x1/9) + (1x1/9) + (0x1/9) + (1x1/9) + (0x1/9) = 6/9 = 0.67
0.67 | 0.67 | 0.78
0.56 | 0.67 | 0.67

## Slide 15: Linear spatial filters
1 | 0 | 1 | 1 | 0
0 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
Simple image matrix
x1/9 | x1/9 | x1/9
x1/9 | x1/9 | x1/9
x1/9 | x1/9 | x1/9
Output matrix
(1x1/9) + (1x1/9) + (1x1/9) + (0x1/9) + (1x1/9) + (0x1/9) + (1x1/9) + (0x1/9) + (1x1/9) = 6/9 = 0.67
0.67 | 0.67 | 0.78
0.56 | 0.67 | 0.67
0.67 |  | 

## Slide 16: Linear spatial filters
1 | 0 | 1 | 1 | 0
0 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
Simple image matrix
x1/9 | x1/9 | x1/9
x1/9 | x1/9 | x1/9
x1/9 | x1/9 | x1/9
Output matrix
(1x1/9) + (1x1/9) + (1x1/9) + (1x1/9) + (0x1/9) + (1x1/9) + (0x1/9) + (1x1/9) + (0x1/9) = 6/9 = 0.67
0.67 | 0.67 | 0.78
0.56 | 0.67 | 0.67
0.67 | 0.67 | 

## Slide 17: Linear spatial filters
1 | 0 | 1 | 1 | 0
0 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
Simple image matrix
x1/9 | x1/9 | x1/9
x1/9 | x1/9 | x1/9
x1/9 | x1/9 | x1/9
Output matrix
(1x1/9) + (1x1/9) + (1x1/9) + (0x1/9) + (1x1/9) + (0x1/9) + (1x1/9) + (0x1/9) + (1x1/9) = 6/9 = 0.67
0.67 | 0.67 | 0.78
0.56 | 0.67 | 0.67
0.67 | 0.67 | 0.67

## Slide 18: Linear spatial filters
1 | 0 | 1 | 1 | 0
0 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
Simple image matrix
Output matrix
0.67 | 0.67 | 0.78
0.56 | 0.67 | 0.67
0.67 | 0.67 | 0.67

## Slide 19: Linear spatial filters-padding
Images/2-paddingTest.txt
What type of padding does imageJ have?

## Slide 20: Linear spatial filters-Additional consideration
Filter kernel
In some image processing filters, the operation is only performed using the central pixel and strong neighbors. You will see an example of this in morphological operations when you have 8 or 4 connectivity.

## Slide 21: Linear spatial filters- Most frequently used ones
Low-pass filters:
High spatial frequesncies of the image: details or noise
Process -> Smooth
Process -> Filters -> mean… Process -> Filters -> Gaussian blur...
High-pass filters:
Process -> Filters -> Unsharp mask…
Edge detection and enhancement:
Process -> Find edges
Process -> Filters -> variance
Images/3-cat.tif
Notes: Local variance responds to edges because edges exhibit lots of change in pixel intensity over a small region.
Variance can be defined over a region (kernel) of any size, while most other edge detectors are limited to a 3x3 region.
Local variance is less sensitive to image noise. A single outlying pixel intensity won’t have too much impact. Pre-smoothing is not required.
Local variance does not respond as much to the intensity profile (shape) of the edge. Therefore, the ‘strength’ of a variance defined edge can be normalized by the local intensity of the object.

## Slide 22: Linear spatial filters- averaging vs gaussian blur
Gaussian
Averaging
Original
Notes: Averaging good for random noise
It is faster
But you will have high frequency artefacts
ß

## Slide 23: Linear spatial filters- Most frequently used ones
1 | 4 | 7 | 4 | 1
4 | 16 | 26 | 16 | 4
7 | 26 | 41 | 26 | 7
4 | 16 | 26 | 16 | 4
1 | 4 | 7 | 4 | 1
Gaussian
(σ=1)
0 | -1 | 0
-1 | 4 | -1
0 | -1 | 0
Laplacian
4-connected
-1 | -1 | -1
-1 | 8 | -1
-1 | -1 | -1
Laplacian
8-connected
-1 | -1 | -1
-1 | 12 | -1
-1 | -1 | -1
Sharpen
-1 | 0 | 1
-2 | 0 | 2
-1 | 0 | 1
Sobel
Horizontal
-1 | -2 | -1
0 | 0 | 0
1 | 2 | 1
Sobel
Vertical
-1 | -1 | -1
0 | 0 | 0
1 | 1 | 1
Prewitt horizontal
-1 | 0 | 1
-1 | 0 | 1
-1 | 0 | 1
Prewitt vertical
Images/3-cat.tif
Try your own filter

## Slide 24: Linear spatial filters- The effect of kernel size and shape on final image
Images/3-cat.tif
Square
Diamond
3x3
5x5
Circle
1 | 1 | 1
1 | 1 | 1
1 | 1 | 1
1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1
7x7
1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1
0 | 0 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0
1 | 1 | 1 | 1 | 1
0 | 1 | 1 | 1 | 0
0 | 0 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0
1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1
0 | 1 | 1 | 1 | 0

## Slide 25: During the lecture
1
How to use linear filtering
Practice with ImageJ Fiji convolve tool
Practice with filters
2
How to use RANK filtering
Practice with ImageJ Fiji RANK filters

## Slide 26: Spatial RANK filters
1 | 0 | 2 | 1 | 0
0 | 0 | 3 | 0 | 1
1 | 1 | 5 | 1 | 1
0 | 4 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
Simple image matrix
Output matrix
5 | 5 | 5
5 | 5 | 5
5 | 5 | 5
0 | 0 | 0
0 | 0 | 0
0 | 0 | 0
1 | 1 | 1
1 | 1 | 1
1 | 1 | 1
Min, Max and Median filters

## Slide 27: Spatial RANK filters
xy_calibrated_16bit__cells_eres_noisy.tif
A mean filter reduces the intensity of the extreme values but spreads out their influence, while a small median filter is capable of removing them completely with a minimal effect upon the rest of the image.
Minimum and maximum filters can be used for uneven background removal.
Task: Try, minimum, maximum, minimum followed by maximum, gaussian blur, and median filters with different radius
Good resource: https://petebankhead.gitbooks.io/imagej-intro/content/chapters/filters/filters.html
Notes: There is more than one way to do image analysis

## Slide 28: Linear spatial filters- median vs gaussian blur
Gaussian blur (3 pix)
Original
Median (3 pix)
No noise
Additive White Gaussian Noise
Salt
and pepper
Higher noise attenuation for Gaussian blur (same radius)
Gaussian blur
spreads out
outliers

## Slide 29: During the lecture
1
How to use linear filtering
Practice with ImageJ Fiji convolve tool
Practice with filters
2
How to use RANK filtering
Practice with ImageJ Fiji RANK filters
3
Practical exercises
Trying uneven background subtraction
Trying noise removal using filters

## Slide 30: When do we use filters? Noise removal
nuclei-noisy.tif
Task: Segment the nuclei in the image
Correct background and remove the noise
MAX_nuclei_noisy-2.tif
Notes: Few things about stacks
Manipulating slices, make a substack and orthogonal view

## Slide 31: When do we use filters? Uneven background correction
TH.tif
Small details (kinetochores, width: 5-6 pixels)
Image from Fabrice
Task: Segment the spots in the image
Let’s look at the image intensity profile first and try what you have learnt yesterday
Use linear filters to remove the background first
Use RANK filters to remove the background
Good sample preparation and image acquisition is always the best way to start!
Notes: Gaussian blur 2, niblack threshold local 50 and 2

## Slide 32: When do we use filters? Uneven background correction
TH.tif
Plot profile

## Slide 33: When do we use filters? Uneven background correction
TH.tif
Plot profile

## Slide 34: When do we use filters? Uneven background correction
TH.tif
Plot profile

## Slide 35: When do we use filters? Uneven background correction
TH.tif
Task: Segment the spots in the image
Use linear filters to remove the background first
1
Duplicate the image
2
Blur the image using one of bluring techniques you learned
3
Subtract the image from the blurred image
4
Plot profile
Notes: Gaussian blur 15
Or median filter

## Slide 36: When do we use filters? Uneven background correction
TH.tif
Task: Segment the spots in the image
Use RANK filters to remove the background
1
Duplicate the image
2
Use minimum filter and subsequently maximum filter (top hat filter)
3
Subtract 1 from 2
4
Plot profile
Notes: Radius 6

## Slide 37: When do we use filters? Uneven background correction
uneven-background-test-image.tif
Autophagosomes.tif
Remember these images from Tischi’s lecture?
Let’s try removing the background using the two methods you just learned
Notes: auto local thresholding is powerful, but it does not remov the background and thus one cannot quantify the intensities. Local background subtraction is better, because it does two things at once: facilitate thresholding but also produces a new image that can be used to quantify the intensities of the small dots. And it is less of a black box algorithm, because one can actually see which background was subtracted. For auto-local-thresholding it is kind of fishing in the dark to find good parameters.

## Slide 38: During the lecture
1
How to use linear filtering
Practice with ImageJ Fiji convolve tool
Practice with filters
2
How to use RANK filtering
Practice with ImageJ Fiji RANK filters
3
Practical exercises
Trying uneven background subtraction
Trying noise removal using filters
4
Morphological operators
Trying different morphological operators

## Slide 39: Morphological operations
Goal: Improve the binary mask obtained by the segmentation to correctly perform morphological analysis.
Need binary image as input.
Some of the morphological operators (morphomaths):
Dilation
Erosion
Opening
Closing
Watershed
Fill holes
…
Double check Edit -> Options -> Colors…

## Slide 40: Morphological operations
Dilation: When the intensity of the center pixel is 1, all the connected pixels are converted to 1.
Gray value equivalent: Maximum
Dilation
https://www.edx.org/course/image-processing-and-analysis-for-life-scientists

## Slide 41: Morphological operations
Erosion: When the intensity of the center pixel is 0, all the connected pixels are converted to 0.
Gray value equivalent: Minimum
Erosion

## Slide 42: Morphological operations
Opening: Erosion followed by Dilation
Removes small objects and separates components.
Closing: Dilation followed by Erosion
Removes small holes and merges components.
Images/Binary.tif
https://imagej.nih.gov/ij/docs/guide/146-29.html
Notes: What does iteration and count mean?
Count Specifies the number of adjacent background pixels necessary before a pixel is removed from the edge of an object during erosion and the number of adjacent foreground pixels necessary before a pixel is added to the edge of an object during dilation.
When you do erosion, analyze particles, even if you click on exclude edges you will still have the edge particles. So pay attention to that.

## Slide 43: Morphological operations
Task: Using morphological operators, make an outline of the image with the thickness of one pixel
Images/Binary.tif

## Slide 44: Morphological operations
Watershed:
Erodes the objects to find the ultimate erode point: objects -> single points
Dilates the points until it reaches the border of the object or the border of another growing object
Good for: homogenous objects with minimal overlap
Images/Binary.tif
Images/Binary2.tif

## Slide 45: Morphological operations
Fil holes:
Good step before watershed
It can also fills the space between objects 
Task: Combine morphological operators to successfully watershed Binary3.tif
Images/Binary.tif
Images/Binary3.tif